## Slide 1
Presenter: Liu XuTong
Team members: Liu JunHan, Dang JiaYing,Liu XuTong,Guo GuangHan,Ning WanZheng
order: Liu XuTong,Liu JunHan,Dang JiaYin,Guo GuangHan,Ning WanZheng
Core idea
Less mass -> less energy demand
Lightweight Recycled Carbon Fiber Carriage Materials for Sustainable High-Speed Rail
Reducing energy use and carbon emissions through lighter carriage design
Notes: Presenter: [Name 1]. Open with the project theme: sustainable high-speed rail technologies. State clearly that the team's final design solution is lightweight recycled carbon fiber carriage materials. The key argument is that reducing carriage mass can reduce operational energy use, which may lower electricity cost and carbon emissions over the long life cycle of Australia's future high-speed rail. Timing guide for a 15-18 minute team presentation: each speaker should speak for at least 2 minutes.

## Slide 2
Context: Australia’s Future High-Speed Rail
Newcastle-Sydney is the case example for this design project.
02
Sources: Infrastructure Australia; High Speed Rail Authority
Presenter:Liu XuTong
Newcastle-Sydney: first major stage
194 km
proposed alignment
Up to 320 km/h
planned speed outside tunnels
Long-term need
energy-efficient and sustainable operation
Newcastle
Central Coast
Sydney
Design focus: lower energy per carriage
Notes: Presenter: [Name 1]. Explain that the project sits inside Australia's future high-speed rail context. Use Newcastle-Sydney as the case example because it is identified as a major early stage. The proposed alignment is 194 km and the planned speed is up to 320 km/h outside tunnels. The design challenge is not only building fast rail, but operating it efficiently and sustainably for decades. Sources: Infrastructure Australia High Speed Rail Newcastle-Sydney evaluation; High Speed Rail Authority corridor context.

## Slide 3
Problem Definition
Heavy carriage materials can increase energy demand across the operating life of high-speed rail.
03
Presenter:Liu JunHan
Problem
Heavy carriages increase lifetime energy and emissions pressure.
Heavier carriage
More mass to move
Higher energy use
More electricity
Higher cost + CO2-e
More pressure
Lower sustainability
Long-term impact
Design target: carriage mass
Notes: Presenter: [Name 2]. Define the problem using the causal chain. The issue is not that current trains cannot work; the issue is that heavy and energy-intensive carriage materials can increase energy use, electricity cost, and operational emissions. This creates sustainability pressure over a long rail operating life. This slide sets up why lightweight materials are a relevant engineering design direction.

## Slide 4
Solutions
Problems mapped to options, then filtered by impact, feasibility, and risk.
Problems
Energy use
C
Carbon pressure
?
Rail safety
Delivery risk
>
Candidate solutions
Recycled CFRP panels
CHOSEN
Direct + testable
!
Fewer stops
NOT SELECTED
Service trade-off
AI
AI dynamic routing
NOT SELECTED
High tech risk
Study pods
NOT SELECTED
Off-scope
Final choice: lightweight recycled CFRP carriage materials
Cuts weight
Lowers energy
?
Can be validated
Presenter: Liu JunHan

## Slide 5
Our Design Solution
Use lightweight, recycled carbon fiber carriage materials for selected components.
05
Sources: Ulbricht et al. 2023
Presenter: Dang JiaYin
Main solution
Recycled CFRP panels
Interior panels
Seat shells
Partitions
Covers
Reduce mass
Less material weight
Lower energy
Less energy demand
Recycle value
Circular material use
Lower risk
Test selected parts first
Lighter carriage -> lower operating energy
Notes: Presenter: [Name 2]. Present the solution clearly: lightweight recycled carbon fiber carriage materials. The idea is to use recycled carbon fiber composite panels in selected carriage components such as interior panels, seat shells, partitions, or non-primary covers. This is a partial substitution that should be tested against strength, fire, safety, maintenance, and certification requirements. Source: Ulbricht et al. 2023 discusses high-performance composite lightweight rail components and the need to meet rail standards.

## Slide 6
Why We Chose This Solution
The selected option performs strongly across sustainability, efficiency, feasibility, and risk control.
06
Presenter: Dang JiaYin
Decision ranking
Sustainability
5/5
Efficiency
5/5
Feasibility
4/5
Risk control
4/5
Implementation ease
4/5
Innovation
4/5
Cost
3/5
Sustainability fit
Circular material use + lower emissions potential
Controlled risk
Start with selected components
High benefit potential + realistic validation
Notes: Presenter: [Name 4]. Explain that the team selected this solution because it scores strongly on sustainability and efficiency, while still being feasible to validate through material and component testing. Cost is lower than the top criteria because recycled CFRP may involve high upfront material, processing, testing, and certification costs. The decision matrix is a design summary, not a precise financial model.

## Slide 7
Base-Case Cost and Carbon Estimate
Visible calculation, but not a guaranteed saving.
Sources: Greengauge 21; AEMO Q4 2025; National Greenhouse Accounts 2025
Presenter: Guo GuangHan
Inputs
194 km route
15m trips/year
0.033 kWh/seat-km
70% load factor
5% saving assumption
A$0.075/kWh
0.67 kg CO2-e/kWh
Estimate inputs
Energy use
15m x 194 x 0.033 / 0.70
= 137.2 GWh/year
Energy saved
137,185,714 x 5%
= 6.86 GWh/year
Cost saved
6,859,286 x 0.075
≈ A$0.51m/year
CO2-e cut
6,859,286 x 0.67 / 1000
= 4,596 t/year
30-year gross electricity saving
≈ A$15.4m
Conclusion
Could save per year:
6.86 GWh | A$0.51m | 4,596 t CO2-e
Gross saving before material, testing, certification, and maintenance costs
Notes: Presenter: [Name 4]. Walk through the calculation step by step. Annual energy use = 15,000,000 x 194 x 0.033 / 0.70 = 137,185,714 kWh/year, or about 137.2 GWh/year. Annual electricity saved = 137,185,714 x 5% = 6,859,286 kWh/year, or about 6.86 GWh/year. Annual electricity cost saving = 6,859,286 x 0.075 = A$514,446/year, or about A$0.51 million/year. Annual CO2-e reduction = 6,859,286 x 0.67 / 1000 = 4,596 tonnes CO2-e/year. Over 30 years this equals about A$15.43 million in gross electricity savings before deducting extra material, testing, certification, and maintenance costs. The figures are base-case estimates, not guaranteed savings. Sources: Greengauge 21 energy benchmark, AEMO Q4 2025 electricity price, Australian National Greenhouse Accounts Factors 2025.

## Slide 8
How the Solution Works
Lightweight recycled CFRP reduces carriage mass while keeping structural performance in selected components.
08
Presenter:Guo GuangHan
Selected carriage panels
Material substitution
Recycled CFRP panels
Mass reduction
Lower carriage weight
Operational effect
Lower energy demand
Life-cycle benefit
Less energy use may reduce cost and CO2-e over long operation.
Key principle: reduce mass without compromising rail safety.
Notes: Presenter: [Name 3]. Explain how the material solution works. The team is proposing recycled CFRP composite panels for selected carriage components. CFRP can provide high strength-to-weight performance, so selected panels can reduce carriage mass while still needing to meet rail safety, fire, durability, and maintenance standards. Lower carriage mass can reduce the energy required during operation, which may reduce electricity cost and CO2-e emissions over the long service life.

## Slide 9
Engineering Validation Plan
The next stage is material, safety, and component testing.
09
Presenter: Guo GuangHan
1
Select components
2
Compare samples
3
Strength testing
4
Fire + safety review
5
Maintenance check
6
Life-cycle analysis
Evidence needed: mass reduction + strength + safety + whole-life value
Notes: Presenter: [Name 3]. Explain the engineering validation plan. The team should first identify suitable non-primary carriage components, compare recycled CFRP samples with conventional materials, test strength and stiffness, review fire and rail safety requirements, check maintenance and repair implications, and then complete a life-cycle cost and carbon analysis. This is appropriate for a final rail materials solution.

## Slide 10
Stakeholder Needs
The same design choice supports different stakeholder priorities.
10
Presenter:Ning WanZheng
Stakeholder
Need
Solution link
Railway operators
Lower cost
Less energy use
Government authorities
Carbon reduction
Lower emissions
Passengers
Reliable green rail
Efficient operation
Local communities
Lower footprint
Lower operational impact
Engineers + manufacturers
Practical innovation
Test selected parts first
Technical performance + sustainability outcomes
Notes: Presenter: [Name 5]. Connect the design to stakeholder needs. Operators care about efficient operation and lower costs; government and transport authorities care about emissions and sustainable infrastructure; passengers need reliable and sustainable services; communities benefit from a lower operational footprint; manufacturers and engineers need practical innovation that can be tested first. The solution meets these needs because it targets energy use through carriage mass reduction.

## Slide 11
Risks, Limitations, and Next Steps
The proposal is promising, but it needs material evidence, cost analysis, and rail-safety validation.
11
Presenter: Ning WanZheng
Risks
Upfront cost
Material supply
Certification
Repair/recycling
Manufacturing changes
Limitations
Material data gaps
Real-train physics
Passenger load
Traction efficiency
Net cost uncertainty
Next steps
Select components
Test CFRP samples
Compare stability
Check rail standards
Life-cycle analysis
Final message: lower carriage mass may reduce energy, cost, and emissions.
Notes: Presenter: [Name 5]. Close by being balanced. The proposal has risks: high upfront material cost, uncertain recycled carbon fiber supply, safety certification, repair and recycling complexity, and manufacturing changes. Real HSR performance also depends on aerodynamics, gradients, passenger loading, and traction efficiency. The next steps are to select suitable components, test recycled CFRP samples, compare stability and durability, research material costs and rail safety standards, and complete a life-cycle cost analysis. End with the core sentence: reducing carriage mass can reduce operational energy use, which may lower electricity cost and carbon emissions over the life cycle.